## Slide 1: CMS Introduction
2006/09/25 by Eric

## Slide 2: Agenda
Installation
Definitions in Configuration
Functions
Product Roadmap
Trouble Shooting

## Slide 3: Installation
Two steps software installation
Check default paths
  “..\CMS\Storage” for Instant Recording
  “..\CMS\Snapshot” for Snapshot
  “..\CMS\Archive” for Remote Archive
Step 1
Step 2

## Slide 4: Definitions in Configuration
Group: a set of mixture of DVR, Video Server and IP Cam
  Up to 10 group(s) w/ different configuratoin
  Unique name of group
  Activation of group
  Messages

## Slide 5: Definitions in Configuration
Site: 4/8/16ch DVR, Video Server and IP Cam
  Up to 64 site(s) in one group
  Unique name of group
  Messages
Settings of Site
Site: 79094
Model: 4ch DVR
Port: 80
Username: user
Password: ****

## Slide 6: Functions (I)
Group/Site Management
  Group
    Add / Rename / Remove
  Site
    Add / Rename / Remove
Users/Connections Management
  Users Authentication
  Max. Connections

## Slide 7: Functions (II)
Basic Operation
  Live Monitoring
  Instant Recording
  Remote Playback/ Local Playback ( in PC )
  Remote Archive
  Settings of DVR
  Snapshot
  Dome Control
System Management ( CMS )
  Site Configuration
  Software Upgrade

## Slide 8: Group Management
Add a group
Rename a group
Remove a group

## Slide 9: Site Management
Add a site
Rename a site
Remove a site

## Slide 10: Add/Configure a site
How to use:
  Move the cursor on the top of menu “add a site” or go to the “Add” button directly
  Configure the setting of Site as below:
Settings of Site
Site: 79094
Model: 4ch DVR
Port: 80
Username: user
Password: ****
#Key in the data as the above and click “OK”
#You can add a new site as you configured

## Slide 11: Users/Connections Management
How to use:
  Username/Password: default value is “user/4321; admin/1234”
  Max. Connections:
    79094: 3 connections (user); 1 connections (admin)
    79100: 3 connections (user); 1 connections (admin)
    7920X: 5 connections (user); 1 connections (admin)
    79216: 5 connections (user); 1 connections (admin)
Settings of Site
Site: 79094
Model: 4ch DVR
Port: 80
Username: user
Password: ****

## Slide 12: Live Monitoring
How to start “Live Monitoring”
  “Start”->”Programs”->”CMS”->”CMS”
  Click the icon “LIVE” on the top
Drag&Drop
Enable/Disable
  Green: enable (default: enable)
  Gray: disable
Mode
Bandwidth

## Slide 13: Instant Recording
Check the “file path”
Start Record
  Click the target channel( mark by yellow square line ) and move cursor to the top of “RECORD” and press
  By using the “pull-down menu”, move to “Record” ->“Start Record”
Stop Record
  Go to pull-down menu to stop record ( “Record” -> “Stop Record” )

## Slide 14: Remote Playback
Start Time
Start Playback
  Press “OK”
Stop Playback
  To stop remote playback by using “Live” on the top of pull-down menu

## Slide 15: Local Playback
Move cursor to the “DVR Player” button
Choose the target *.drv file and double click that row

## Slide 16: Remote Archive
Select radio button “Archive”
Choose a period ( start and end time )
Click “OK” and start to archive files

## Slide 17: Snapshot
Check the “File path” for snapshot
Click “Snapshot” button ( w/ date/time in 2x2, 3x3 and 4x4 mode )
File format
  BMP
  JPG ( default )
  GIF
  TIFF

## Slide 18: Dome Control
Browser based Dome Control
Dome Control via DVR
Internet
RS485

## Slide 19: System Management
Site configuration
  Import
  Export
Software Upgrade
  Export the system configuration( configure file )
  Uninstall installed CMS
  Install latest CMS
  Import the system configuration ( configure file )

## Slide 20: Product Roadmap
Supports Video Server, IP Cam
Multi-level users access control ( CMS )
Remote Event Handling
  Local/Remote Event Playback
  Local/Remote Event Search
  Remote Event Archive
DVR Monitoring ( status report )
Audio
Alert

## Slide 21: Trouble Shooting
How to restart the CMS program when you see the dialogue as below ?